## Slide 1
LINE FOLLOWING
ROBOT CAR
Autonomous Navigation · Bluetooth Remote Control · Live Camera Feed
Ahror Nosirov · Jamshid Vakhobov · Islomov Jaxongir
Arduino SMARS Platform | 2026
Line Following Robot Car — Project Presentation

## Slide 2
Project Overview
What we built and why
What is it?
A 3D-printed SMARS robot car that can autonomously follow a black line on a white surface, or be driven manually from a smartphone.
Why we built it?
To explore embedded systems, sensor integration, wireless communication, and real-time control in a single hands-on project.
What makes it special?
Three modes in one compact robot: fully autonomous line tracking, bluetooth remote control, and live ESP32-CAM video streaming.
[AUTO] AUTO MODE
Searches for & follows the line autonomously
[APP] REMOTE MODE
Bluetooth control via mobile app
[CAM] LIVE CAMERA
ESP32-CAM streams real-time video

## Slide 3
Components Used
Everything that makes the robot work
ARDUINO UNO
The brain of the robot — runs all control logic and coordinates sensors, motors, and communication.
2× DC MOTORS
Drive the left and right wheels for forward, backward, and turning motion.
MOTOR DRIVER
L298N bridge driver — translates Arduino PWM signals into motor power.
3× IR SENSORS
HW-511 infrared modules detect black/white contrast to locate the line (left, center, right).
HC-06 BLUETOOTH
Receives commands from the mobile app for remote control mode.
ESP32-CAM
Wi-Fi camera module — streams live first-person video to the mobile device.
9V KRONA BATTERY
Portable power supply for the entire system.
SMARS CHASSIS
3D-printed modular chassis with tank-track Mecanum-style wheels.

## Slide 4
Chassis & Physical Design
SMARS — Screwless Modular Assemblable Robotic System
3D Printed SMARS Chassis
Open-source, fully 3D-printable robot platform designed for modularity.
Colorful Multi-Part Build
Printed in multiple colours (blue, green, yellow, orange, white) using FDM printing.
Tank-Track Wheel System
Custom interlocking track segments provide stable traction on flat surfaces.
Sensor Mount at Front
Three IR sensors mounted in a row at the front-bottom for accurate line detection.
Compact Stacked Layout
Motor driver, Arduino, and Bluetooth module stacked vertically inside the chassis to save space.
INSERT PHOTO
[Insert side/front chassis photo]

## Slide 5
Electronics & Wiring
How all the components connect together
IR Sensors → Arduino
3 HW-511 IR modules → Digital pins D2, D3, D4
Arduino → Motor Driver
PWM pins → L298N IN1/IN2/IN3/IN4 + ENA/ENB
Motor Driver → Motors
OUT1/OUT2 → Left motor | OUT3/OUT4 → Right motor
HC-06 → Arduino
TX → RX (pin 0) | RX → TX (pin 1)
ESP32-CAM → System
Independent Wi-Fi module powered from 5V rail
9V Battery → Motor Driver
VIN on L298N | 5V regulator output → Arduino & logic
INSERT PHOTO
[Insert wiring / top-view photo]

## Slide 6
How Line Following Works
IR sensor logic & decision algorithm
IR SENSOR STATES & MOTOR RESPONSE
LEFT
CENTER
RIGHT
→ ACTION
⚫ sees line
⚫ sees line
⚫ sees line
→ Go FORWARD (on line)
⚫ sees line
⚪ off line
⚪ off line
→ Turn LEFT
⚪ off line
⚪ off line
⚫ sees line
→ Turn RIGHT
⚪ off line
⚫ sees line
⚪ off line
→ Go FORWARD
⚪ off line
⚪ off line
⚪ off line
→ SEARCH (slow spin)
Algorithm Flow
1. Read all 3 IR sensor values (HIGH = white, LOW = black line)
2. Evaluate combination against look-up table
3. Send PWM speed values to motor driver
4. Loop every ~10 ms for smooth real-time tracking
5. If all sensors lose line → slow spin to search & re-acquire
Sensor Layout (Front View)
LEFT Sensor
CENTER Sensor
RIGHT Sensor
← black line on white surface →

## Slide 7
Operating Modes
Two modes, one robot — switchable from the app
[AUTO] AUTO MODE
• Activated by tapping AUTO in the mobile app
• Robot reads 3 IR sensors continuously
• Steers left/right to stay on the black line
• If line is lost, enters search mode (slow rotation) until line is re-found
• Speed is adjustable via the app slider
• Fully hands-free once activated
[APP] REMOTE MODE
• Activated by tapping MANUAL in the mobile app
• HC-06 Bluetooth module receives commands
• Commands: Forward, Backward, Left, Right, Stop
• App sends single-character codes (F, B, L, R, S)
• Arduino parses command & drives motors accordingly
• IR sensors are ignored in this mode
OR

## Slide 8
Mobile App & Bluetooth Control
HC-06 module + Android app
App Interface
Custom Android app with directional buttons, mode switch (Auto/Manual), speed slider, and live camera view.
Bluetooth Connection (HC-06)
HC-06 is a classic Bluetooth 2.0 serial module. Pairs with smartphone like any Bluetooth device. Range: ~10 metres.
Command Protocol
Simple single-byte serial protocol:
F = Forward B = Backward L = Turn Left
R = Turn Right S = Stop A = Auto mode
Response Time
Near real-time response (~50–100 ms latency) — fast enough for smooth manual driving.
Safety
Robot stops automatically if Bluetooth connection is lost.
App Layout (Schematic)
^ FORWARD
< LEFT
RIGHT >
v BACK
[] STOP
AUTO MODE * MANUAL MODE
SPEED: =======O 80%
[CAM] Live Camera Feed (ESP32-CAM stream)

## Slide 9
ESP32-CAM Live Video Feed
First-person real-time streaming from the robot
Module: ESP32-CAM
Compact Wi-Fi + camera module with OV2640 image sensor. Operates independently from the Arduino.
Streaming Method
Runs an MJPEG HTTP server over Wi-Fi. The mobile app connects to the ESP32's IP and displays the stream.
Why it's useful
Lets the operator see what the robot sees — useful for remote driving in unknown environments.
Resolution & FPS
Up to 1600×1200 px | ~15–25 fps over local Wi-Fi.
Power
Powered from the 5V regulated rail of the motor driver — no separate battery needed.
[ Live Camera View ]
[CAM] ESP32-CAM | MJPEG Stream
* REC

## Slide 10
Building Process
From idea to working robot — step by step
1
Design & Plan
>
Chose SMARS platform, listed components, drew wiring diagram.
2
3D Printing
>
Printed chassis parts in multiple colours using FDM. Track segments, body, mounts.
3
Assembly
>
Assembled chassis, fitted motors, attached wheels/tracks and sensor bracket.
4
Electronics
Wired motor driver, IR sensors, HC-06, ESP32-CAM to Arduino. Soldered connections.
5
Programming
>
Wrote Arduino sketch: line-follow logic, Bluetooth command parser, motor control.
6
App Development
>
Built Android app with Bluetooth controls, mode switch, and camera view.
7
Testing & Tuning
Tested on black tape track. Tuned sensor sensitivity, speed, and turn sharpness.
v

## Slide 11
Challenges & Solutions
Problems we faced and how we solved them
! IR Sensor Calibration
Problem: Sensors gave inconsistent readings on different floor surfaces.
OK Added adjustable sensitivity potentiometer on each HW-511 module. Fine-tuned threshold for the test track.
! Wiring Complexity
Problem: Too many wires caused shorts and loose connections inside the cramped chassis.
OK Colour-coded wires, used DuPont connectors, and routed cables along chassis walls.
! Bluetooth Latency
Problem: Occasional lag in remote control made driving imprecise.
OK Kept command strings short (1 byte). Improved app's send rate to 100 ms polling.
! ESP32-CAM Power
Problem: Camera module caused Arduino to reset due to current spike on startup.
OK Powered ESP32-CAM from dedicated 5V output on motor driver board, separate from Arduino.
! Sharp Turns on Track
Problem: Robot overshot corners at high speed.
OK Reduced turn speed via PWM differential and added a small delay at detected curves.

## Slide 12
Results & Live Demo
What the robot achieved
3
IR Sensors for line detection
2
Operating Modes
~10m
Bluetooth range
15–25
FPS camera stream
Achievements
OK Successfully follows a black line on white surface at various speeds
OK Smooth mode switching between Auto and Manual from the mobile app
OK Real-time Bluetooth response — commands execute within 50–100 ms
OK ESP32-CAM streams live video without interrupting main robot logic
OK Robot recovers from lost line by entering search / slow-spin mode
OK Robust 3D-printed chassis — survived multiple drops and track tests

## Slide 13
Thank You!
Questions & Live Demo
Our Team
Ahror Nosirov
Jamshid Vakhobov
Islomov Jaxongir
Line Following Robot Car - Arduino SMARS - 2026